## Slide 1: System Programming
Design and Implementation of system software.
System Software: a variety of programs supporting the operation of a computer.
Typical system programs: OS, Complier, Assembler (Linker, Loader, Macro Processors), Text Editor, Debugger, …,
  Their functions and relations among them?
Why specific and important:
  rely on hardware (computer architecture)
  need related low level languages such as assembly language
  Free users from knowing the detail of machines.

## Slide 2: Relations?
Programming Languages:
  Machine Language (ML) Assembly Language (AL) High-Level Programming Language (HL)
    ML: machine code, i.e, binary code, e.g., 01100110
    AL: mnemonic instructions, e.g., STO (Store)
    HL: statements, e.g. if … Then … else …
  Programs in HL  Object Code (in AL or ML)
            (Compiler)
  Programs in AL  Object Code (in ML)
            (Assembler)
Four typical systems
  Operating System, Compiling System, Database (Administration) System, Network System

## Slide 3: Relations?
Type and modify a program in HL or AL (by an editor)
Translate it into object code in ML (by a compiler or assembler)
Load it into memory for execution (by a linker and/or loader)
Execute it on CPU (by an OS)
Detect errors in the code (by a debugger)
All the processes and programs are run under and controlled by an OS such as Windows or Linux.
IDE (Integrated Development Environment)

## Slide 4: Topics
Assembly language and its programming
Structure (architecture) of machines.
Assembler
Linker, Loader, Macro Processor
Compiler
Others (OS, Editor, DB, network, SE, if time allowed)

## Slide 5: System software and Machine Architecture
One main characteristic in which system software differs from application software: machine dependence.
  Assembler: instruction format, addressing modes
  Compiler: registers (number, type), machine instructions
  OS: all of the resources of a computing system.
Of course, some aspects of system software are machine-independent.
  General design and logic of a assembler
  Code optimization in a compiler
  Linking of independently assembled subprograms.

## Slide 6: Dilemma? And SIC
Since for system software which is machine dependent, there is a need for real machine
However, most real machines have certain characteristics which are unusual or unique.
Very difficult to distinguish the features which are fundamental and those which are idiosyncrasies of a particular machines.
In addition, so many machines
So SIC: Simplified Instructional Computer

## Slide 7: Sections of major chapters
Fundamental functions
Features depending on machine
Features which are common and machine-independent
Major design principles and options
  Such as single pass or multiple passes.
Examples of actual implementations on real machines
  SIC, SIC/XE (Extra equipment, upward compatible)
  CISC (Complex Instruction Set Computers) : VAX, Pentium Pro
  RISC (Reduced Instruction Set Computers): UltraSPARC, PowerPC, Cray T3E

## Slide 8: SIC architecture
Memory:
  8-bit bytes, total 32,768 (215) bytes.
  Word: any 3 consecutive bytes
  Addressing:
    any byte
    Word: the lowest byte
Registers:
  Five, A, X, L, PC, SW, (0,1,2,8,9) , 24 bits each
  A: accumulator for arithmetic operations, X: index, for address, L: Linkage, store the return address when JSUB jumps to a subroutine
  PC:: program counter, the address of next instruction for fetch and execution, SW: Status Word, including condition code (CC)
Data Formats:
  Integers: 24 bits, 2’s complement for negative numbers
  Chars: 8-bit ASCII codes.
  No floating-point numbers.
Instruction Formats
  Opcode (8) + x(1) + address (15), x: addressing mode
Addressing modes:
  Direct addressing, x=0, Target Address (TA) =address
  Indexed addressing: x=1, TA=address+(X), address in the instruction plus Index Register
Instruction Set:
  Load and Store Registers: LDA, LDX, STA, STX, etc.
  Integer Arithmetic: ADD, SUB, MUL, DIV, all these operation involve register A and a word in memory, and the result is in A.
  COMP: compare A with a word, and set the result (<, =, >) in Condition Code (CC) in SW.
  Conditional jump instructions: JLT, JEQ, JGT, test CC and jump accordingly
  Subroutine linkage instruction: JSUB and RSUB. JSUB jumps to the subroutine and places the return address in L, RSUB returns by jumping to address in L.
Input/Output:
  IO devices: each is assigned a unique 8-bit code.
  All input/outputs are between the rightmost 8 bits of A and a device.
  Three instructions (with device code as operand, i.e., in the address of the instruction)
    TD (Test Device) : whether the device is ready, condition code is set: 1: ready, 0: not ready
    RD (Read Data) and WD (Write Data): a program must wait until a device is ready to transfer data

## Slide 9: SIC/XE architecture
Memory:
  Total 1M (220) bytes. So need change the instruction formats and addressing modes.
Registers:
  Four more: B, S, T, F (3,4,5,6).
  B: Base register, for addressing, S: general working register, T: general working register, F: floating-point accumulator (48 bits)
Data Formats:
  In addition, 48-bit floating-point numbers: s(1)+exponent(11)+fraction(36), the absolute value will be f*2(e-1024)
Instruction Formats
  Mode 1 (1 byte): op (8), Mode 2 (2 bytes): op(8)+r1(4)+r2(4)
  Mode 3(3 bytes): op(6)+n(1)i(1)x(1)b(1)p(1)e(1)+disp(12)
  Mode 4(4 bytes): op(6)+n(1)i(1)x(1)b(1)p(1)e(1)+address(20), e=0: mode 3 and e=1: mode 4.
Addressing modes (two new relative addressing):
  Base relative: b=1,p=0, TA=(B)+disp (0 ≤ disp ≤ 4095)
  Program –counter relative: b=0, p=1, TA=(PC)+disp (-2048 ≤ disp ≤ 2047)
  b=0, p=0: TA=disp. Called direct addressing, wrt. Relative addressing.
  In Mode 4, usually b=0 and p=0, and TA =address. Also called direct addressing., wrt. Relative addressing.
  x=1, then (X) is added. Called indexed addressing.
  i=1, and n=0: TA is an operand, no memory reference. So called immediate addressing.
  i=0 and n=1: the operand is the value in the address which is the value in the address indicated by TA., called indirect addressing.
  i=0 and n=0 or i=1 and n=1: the TA is the address of the operand. Called simple addressing.
  Distinguish different addressing modes:
  Indexed addressing cannot be used with immediate or indirect addressing modes.
  i=1 and n=1: for SIC/XE with non immediate or indirect addressing,
  i=0 and n=0: for SIC, which will keep upward compatibility. In this case, b,p,e bits will be treated as part of 15 bit address (rather than as addressing flags).
Instruction Set (additional):
  Load and Store to new registers, e.g., LDB, STB, etc.
  Floating-point arithmetic: ADDF, SUBF, MULF, DIVF
  Operations among registers: ADDR, SUBR, MULR, DIVR
  SVC (Supervisor call): generates an interrupt that can be used for communication with OS.
Input/Output:
  SIO, TIO, HIO: start, test, and halt IO. These allows the parallel of IO and computing.

## Slide 10: Machine language, Assembly Language and AL programming
Example of SIC/XE instructions and addressing modes
  Machine language, binary codes
  Different addressing modes
  Most basic operations and direct memory locations
  Machine structure
  Code and data both are binary.
  (note: the five instruction 003600 is SIC one)
  Simple data movement operations for (a) SIC and (b) SIC/XE (Fig1.2-Page13)
    Symbol (mnemonic) instruction
    Data (its location) is referred by label.
    Direct mapping between mnemonic instruction and machine code.
    Later, Macro functions and subroutines.
    Codes areas and data areas.

## Slide 11: SIC Assembly Language Programs
assembler directives
  START, END, BYTE, WORD, RESB, RESW, BASE, …
Simple arithmetic operations for (a) SIC and (b) SIC/XE
  What is the function of the program?
Simple looping and indexing operations for (a) SIC and (b) SIC/XE
Another Simple looping and indexing operations for (a) SIC and (b) SIC/XE
Simple Input and Output operations for SIC
Simple subroutine call and record input operations for (a) SIC and (b) SIC/XE

## Slide 12: Traditional (CISC) machines
Large and complicate instruction set, many different instruction formats and lengths, many addressing modes.
VAX (DEC):
  Word, longword, quadword, octword,
  Word alignment
  Virtual address space—system space and process space
  Stacks
  Many registers, data formats, variable-length instruction formats, many addressing modes
  I/O space is part of physical address space

## Slide 13: CISC—Pentium Pro architecture (Intel)
Intel x86 family
Segments: so address is: segment:offset
Stacks: SP:offset
Pages
Eight general purpose registers, several special-purpose registers, and FPU (floating-point unit) with eight 80-bit registers
Little-endian: least significant part of a value is stored at the lowest numbered address.
Single, double, and extended precision.
Eight addressing modes:
  TA=(base register) + (index register)*scale + displacement
Over 400 instructions, including memory-to-memory
EAX register I/O port (byte, word, double word, repetition for string)

## Slide 14: RISC
Number of machine instructions, instruction formats, and addressing modes are small (standardized, fixed, single-cycle execution)
Memory access are done by just load and store instructions
All other instructions are register-to-register
Large number of general registers.

## Slide 15: RISC—UltraSPARC (Sun Microsystems)
Virtual address space, pages
Over 100 general purpose registers
Any procedure can access only 32 registers.
Support both big-endian and little-endian
Three basic instruction formats with 32 bits long.
Immediate mode, register mode, PC-relative, Register indirect with displacement, Register indirect indexed
Less than 100 instructions
Pipelined execution of instructions
“atomic” instructions that can execute without allowing other memory accesses to intervene.
No special I/O instructions, I/O port and registers are port of memory.

## Slide 16: RISC—PowerPC (IBM)
Virtual address space 264. Segments of fix length 256M each, pages of fix length 4096 bytes.
32 general purpose registers.
Seven instruction formats with 32 bit length
Two modes: immediate and register.
All memory access is via load, store operation and branch instructions with three addressing modes.
200 instructions, some are more complicated than typical RISC such as “multiply and add” with 3 operands.
Two I/O access modes:
  Direct-store access: I/O port and registers as part of physical address
  Virtual memory access: performed by normal virtual memory management hardware and software.

## Slide 17: RISC—Cray T3E (Cray Research Inc.)
Parallel processing
A three dimension network of processing elements (PE)
Each PE consists of a DEC Alpha EV5 RISC microprocessor, local memory and performance-accelerating control logic.
Local memories form a large distributed share memory.
Registers, Data Formats, Instruction formats, addressing modes, instruction set are as normal as RISC
I/O: via multiple ports organized into channels. Each channel is accessible by all PEs.